## Slide 1
University Collaboration and Technology Promotion on Digital Twins Trend in Automotive Industry
CARLA CONTEST 2023

## Slide 2
Agenda
Background & Purpose
Digital Twins
  What are Digital Twins?
  Benefit
  Fundamental Technologies
CARLA
  What is CARLA?
  How does CARLA Work?
  CARLA Components
Autonomous Driving
  What is Autonomous Driving?
  Autonomous Driving Example
  Autonomous Driving Knowledge Overview
  Autonomous Driving Sensors
  Sensors for Contest
Demo
Appendix

## Slide 3
Background & Purpose
Currently, the automotive industry is moving toward the mobility innovation of the future which can refer to “CASE” framework (Connected, Autonomous, Sharing, Electric). The Digital Twins technology is one of the keys technology for this innovation.
Thus, the automotive requirement is more complex as well as testing scenario. In order to fulfill these requirements, the system & software development method has to be evolved and “Digital Twins” is one the key technology for this evolution in automotive industry.
We aim to promote digital twins trend of automotive software development industry and encourage university student to build career in automotive software development industry in Thailand.

## Slide 4
Digital Twins

## Slide 5
A digital twins are a digital representation of a physical object, process or system.
A digital twins are a computer program that uses real world data to create simulations, study performance issues and generate possible improvements which can then be applied back to the original physical object.
Reference: https://www.mdpi.com/2571-5577/5/4/65/htm
What are Digital Twins?

## Slide 6
Benefit
No. | Type | Benefit
1 | Process | Digital twins can help to mirror and monitor production systems that are all synchronized to operate at peak efficiency, or will delays in one system affect others.
2 | Product | ADAS architecture is increased the ability to respond or detect threats by the knowledge obtained from sensor data stored on cloud and processed on digital twin.
3 | Service | Manufacturer maintains a digital record of the working condition of the car and also detects potential problems that are being fixed by simply downloading over-the-air (OTA) software updates.

## Slide 7
Fundamental Technologies
To compute large data collected from sensors with high performance processor
To analyze data, generate behaviors model, and decision making in digital twin.
To provide the connection and access to the physical world and interlink with digital twin
To represent appearance and behaviors of the physical object in digital twin
To detects a physical parameter of interest and converts it into electrical signal that can be measured
Reference: https://www.mdpi.com/2571-5577/5/4/65/htm

## Slide 8
CARLA

## Slide 9
CARLA is an open-source simulator for autonomous driving research that provides open digital
assets, flexible specification of sensor suites and environmental conditions to support development,
training, and validation of autonomous driving systems.
This virtual simulator is also part of digital twins concept. We are going to conduct the workshop in
order to create own autonomous driving control software and run simulation on CARLA
environment.
.
Reference: https://carla.readthedocs.io/en/latest/start_introduction
What is CARLA?

## Slide 10
The CARLA simulator consists of a scalable client-server architecture.
The server is responsible for everything related with the simulation itself: sensor rendering, computation of physics, updates on the world-state and its actors and much more. As it aims for realistic results.
The client side consists of a sum of client modules controlling the logic of actors on scene and setting world conditions. This is achieved by leveraging the CARLA API (in Python or C++).
Reference: https://carla.readthedocs.io/en/latest/start_introduction/
How does CARLA Work?

## Slide 11
Traffic Manager: A built-in system that takes control of the vehicles besides the one used for learning. It acts as a conductor provided by CARLA to recreate urban-like environments with realistic behaviors.
Sensors: Vehicles rely on them to dispense information of their surroundings. In CARLA they are a specific kind of actor attached the vehicle and the data they receive can be retrieved and stored to ease the process. Currently the project supports different types of these, from cameras to radars, lidar and many more.
Traffic Scenario: In order to ease the learning process for vehicles, CARLA provides a series of routes describing different situations to iterate on. These also set the basis for the CARLA challenge, open for everybody to test their solutions and make it to the leaderboard.
Reference: https://carla.readthedocs.io/en/latest/start_introduction/
CARLA Components

## Slide 12
Autonomous Driving

## Slide 13
Autonomous driving is the system that supports driving with limited human intervention by using sensors, cameras, and artificial intelligence.
Level of Autonomous Driving
What is Autonomous Driving?
Reference: :https://https://www.synopsys.com/automotive/what-is-autonomous-car.html/

## Slide 14
Autonomous Driving Example
Reference: https://www.toyota.com/safety-sense/
Pre-Collision System with Pedestrian Detection
Pre-Collision System with Pedestrian Detection (PCS w/PD) is designed to help detect a vehicle or pedestrian and provide an audio/visual forward-collision warning under certain circumstances. If you don’t react, the system is designed to provide automatic emergency braking.
Dynamic Radar Cruise Control
Dynamic Radar Cruise Control (DRCC) is an adaptive cruise control system that uses vehicle-to-vehicle distance control to help maintain a preset distance from the vehicle ahead of you.

## Slide 15
Autonomous Driving Example
Reference: https://www.toyota.com/safety-sense/
Lane Departure Alert
When white/yellow lane markings are detected at speeds within the systems operating range, Lane Departure Alert (LDA) * is designed to issue an audio/visual lane departure warning if an inadvertent lane departure is detected.
Lane Tracing Assist
Lane Tracing Assist (LTA) uses the lines on the road and/or preceding vehicles to provide active driving assistance and help keep the vehicle centered and in its lane.

## Slide 16
Autonomous Driving
Knowledge Overview
Perception
Path planning
A challenge of self-driving cars development is to detect road object for build the occupancy map.
Vehicle needs to consider the feasible path to avoid the obstacle or decided to stop for the pedestrian.
Concept

## Slide 17
Vehicle Actuation
Lateral Dynamics
Longitudinal Dynamics
Vehicle Dynamics
Autonomous Driving
Knowledge Overview

## Slide 18
Feedback – Closed Loop
PID Control
Model Predictive Control
Basic Controller Design
Autonomous Driving
Knowledge Overview

## Slide 19
Sensor Fusion With Kalman Filter
Ego Location Estimation
Autonomous Driving
Knowledge Overview

## Slide 20
Density-Based Spatial Clustering of Applications with Noise (DBSCAN)
Clustering
Radar inverse sensor model
Sensor fusion
Sensor Data Processing
Autonomous Driving
Knowledge Overview

## Slide 21
Autonomous Driving Sensors
Camera: provides realistic images that automatically detect objects, classify them.
Radar: to determine distance between object and sensor.
Lidar: more accuracy than radar and possible to build exact 3D models of objects surrounding vehicle.
GNSS (GPS): used for navigation and positioning measurements.

## Slide 22
Sensors for Contest
Camera
LIDAR
RADAR
Inertial Measurement Unit
Sattellite location
Other sensors: carla.readthedocs.io/en/latest/ref_sensors

## Slide 23
Sensors for Contest
Monocular Camera
Stereo Camera
Camera Calibration Process
Camera Module In TOYOTA’s car

## Slide 24
Sensors for Contest
RGB Camera
Semantic Ground Truth
CARLA Camera

## Slide 25
Sensors for Contest
RGB Image
RGB Image
Semantic Segmentation Labeled
Semantic Segmentation Labeled
Ground Truth
Prediction
Improved computational speed
Reduced complexity / cost
CARLA Camera

## Slide 26
Sensors for Contest
# Set initial camera translation camera_init_trans = carla.Transform(carla.Location(z=2)) # Add one of each type of camera camera_bp = bp_lib.find('sensor.camera.rgb') camera = world.spawn_actor(camera_bp, camera_init_trans, attach_to=vehicle)
# Define respective callbacks def rgb_callback(image, data_dict): data_dict['rgb_image'] = np.reshape(np.copy(image.raw_data), (image.height, image.width, 4)) # Initialise parameters and data image_w = camera_bp.get_attribute("image_size_x").as_int() image_h = camera_bp.get_attribute("image_size_y").as_int() sensor_data = {'rgb_image': np.zeros((image_h, image_w, 4))}
# Set sensors recording camera.listen(lambda image: rgb_callback(image, sensor_data))
1. Initial sensor
2. Define sensor callback function and data buffer
3. Start recording sensor data
CARLA Camera Coding Example

## Slide 27
Sensors for Contest
Lidar (Light Detection and Ranging) is used the laser beam to measure the distance between sensor and an object.

## Slide 28
Sensors for Contest
# Set up LIDAR, parameters are to assisst visualisation lidar_bp = bp_lib.find('sensor.lidar.ray_cast') lidar_bp.set_attribute('range', '100.0') lidar_bp.set_attribute('noise_stddev', '0.1') lidar_bp.set_attribute('upper_fov', '15.0') lidar_bp.set_attribute('lower_fov', '-25.0') lidar_bp.set_attribute('channels', '64.0') lidar_bp.set_attribute('rotation_frequency', '20.0') lidar_bp.set_attribute('points_per_second', '500000') lidar_init_trans = carla.Transform(carla.Location(z=2)) lidar = world.spawn_actor(lidar_bp, lidar_init_trans, attach_to=vehicle)
def lidar_callback(point_cloud, point_list): """Prepares a point cloud with intensity colors ready to be consumed by Open3D""" data = np.copy(np.frombuffer(point_cloud.raw_data, dtype=np.dtype('f4'))) data = np.reshape(data, (int(data.shape[0] / 4), 4)) # Isolate the intensity and compute a color for it intensity = data[:, -1] intensity_col = 1.0 - np.log(intensity) / np.log(np.exp(-0.004 * 100)) int_color = np.c_[ np.interp(intensity_col, VID_RANGE, VIRIDIS[:, 0]), np.interp(intensity_col, VID_RANGE, VIRIDIS[:, 1]), np.interp(intensity_col, VID_RANGE, VIRIDIS[:, 2])] points = data[:, :-1] points[:, :1] = -points[:, :1] point_list.points = o3d.utility.Vector3dVector(points) point_list.colors = o3d.utility.Vector3dVector(int_color)
1. Define sensor callback function
2. Config sensor parameters
CARLA LIDAR Coding Example

## Slide 29
Sensors for Contest
Phased-Array Radar
Attribute | Description
horizontal_fov | Horizontal field of view in degrees.
points_per_second | Points generated by all lasers per second.
range | Maximum distance to measure/raycast in meters.
sensor_tick | Simulation seconds between sensor captures (ticks).
vertical_fov | Vertical field of view in degrees.
Radar (Radio Detection and Ranging) is a radiolocation system that uses radio waves to determine the distance (ranging), angle (azimuth), and radial velocity of objects relative to the site.

## Slide 30
Sensors for Contest
# Set up RADAR, parameters are to assisst visualisation radar_bp = bp_lib.find('sensor.other.radar') radar_bp.set_attribute('horizontal_fov', '30.0') radar_bp.set_attribute('vertical_fov', '30.0') radar_bp.set_attribute('points_per_second', '10000') radar_init_trans = carla.Transform(carla.Location(z=2)) radar = world.spawn_actor(radar_bp, radar_init_trans, attach_to=vehicle)
def radar_callback(data, point_list): radar_data = np.zeros((len(data), 4)) for i, detection in enumerate(data): x = detection.depth * math.cos(detection.altitude) * math.cos(detection.azimuth) y = detection.depth * math.cos(detection.altitude) * math.sin(detection.azimuth) z = detection.depth * math.sin(detection.altitude) radar_data[i, :] = [x, y, z, detection.velocity] intensity = np.abs(radar_data[:, -1]) intensity_col = 1.0 - np.log(intensity) / np.log(np.exp(-0.004 * 100)) int_color = np.c_[ np.interp(intensity_col, COOL_RANGE, COOL[:, 0]), np.interp(intensity_col, COOL_RANGE, COOL[:, 1]), np.interp(intensity_col, COOL_RANGE, COOL[:, 2])] points = radar_data[:, :-1] points[:, :1] = -points[:, :1] point_list.points = o3d.utility.Vector3dVector(points) point_list.colors = o3d.utility.Vector3dVector(int_color)
1. Define sensor callback function
2. Config sensor parameters
CARLA RADAR Coding Example

## Slide 31
Sensors for Contest
Global Navigation Satellite System (GNSS)
Commonly known as GPS (Global Positioning System)

## Slide 32
Sensors for Contest
# Add navigation sensor gnss_bp = bp_lib.find('sensor.other.gnss') gnss_sensor = world.spawn_actor(gnss_bp, carla.Transform(), attach_to=vehicle)
def gnss_callback(data, data_dict): data_dict['gnss'] = [data.latitude, data.longitude]
# Start sensors recording data gnss_sensor.listen(lambda event: gnss_callback(event, sensor_data))
# Initialise data
sensor_data = {'gnss': [0, 0],}
1. Initial sensor
2. Define sensor callback function and data buffer
3. Start recording sensor data
CARLA Navigation Coding Example

## Slide 33
Sensors for Contest
Inertial Measurement Unit (IMU) is a device that typically consists of gyroscopes to measure and report angular rate and accelerometers to measure and report specific force.

## Slide 34
Sensors for Contest
# Add inertial measurement sensor imu_bp = bp_lib.find('sensor.other.imu') imu_sensor = world.spawn_actor(imu_bp, carla.Transform(), attach_to=vehicle)
def imu_callback(data, data_dict): data_dict['imu'] = { 'gyro': data.gyroscope, 'accel': data.accelerometer, 'compass': data.compass }
# Start sensors recording data imu_sensor.listen(lambda event: imu_callback(event, sensor_data))
# Initialise data
sensor_data = { 'imu': { 'gyro': carla.Vector3D(), 'accel': carla.Vector3D(), 'compass': 0 }}
1. Initial sensor
2. Define sensor callback function and data buffer
3. Start recording sensor data
CARLA IMU Coding Example

## Slide 35
Demo

## Slide 36
Q&A

## Slide 37
Appendix

## Slide 38
Resource
Online Introduction Document
CARLA Installer
Video Demo
Supplement Information
CARLA Installer (Map)